## Slide 1: MATLAB Graphics: Basic Plots
Professor Bo Liu
James Watt School of Engineering

## Slide 2: Example plot - 1
time = linspace(0, 10, 21); % matrix of 21 elements between 0 and 10
acceleration = 9.81 * ones(1, 21); % matrix of 21 elements equal to 9.81
plot(time, acceleration) % line plot
See live script for similar examples

## Slide 3: Example plot - 2
title("Acceleration in a vacuum on Earth's surface")
See live script for similar examples

## Slide 4: Example plot - 3
xlabel("Time (s)")
See live script for similar examples

## Slide 5: Example plot - 4
ylabel("Acceleration (m/s^2)")
See live script for similar examples

## Slide 6: Example plot - 5
grid()
See live script for similar examples

## Slide 7: Example plot - 6
hold on % tell MATLAB to put next plots onto same figure
scatter(time, acceleration)
See live script for similar examples

## Slide 8: Example plot - 7
legend(["line", "data points"])
See live script for similar examples

## Slide 9: Thanks!
#UofGWorldChangers
@UofGlasgow

## Slide 10: Plot customization
MATLAB supports many ways of customizing plots.
The easiest way is to add other arguments to the “plot” function call.
Color | Marker | Line style
‘y’  yellow | ‘.’  point | ‘-’  solid
‘m’  magenta | ‘o’  circle | ‘:’  dotted
‘c’  cyan | ‘x’  x-mark | ‘-.’  dashdot
‘r’  red | ‘+’  plus | ‘--’  dashed
‘g’  green | ‘*’  star | 
‘b’  blue | ‘s’  square | 
‘w’  white | ‘d’  diamond | 
‘k’  black | ‘v’  triangle (down) |